## Slide 1: Lab 5: Watersheds

## Slide 2: Watersheds
Define the area of land that contributes water to a stream/river
  Drainage basin
  Identifies highest points surrounding a river

## Slide 4: Watersheds
  Topographic maps can help us delineate watershed boundaries
  Review from lab 1:
Contour lines- lines connecting points of same elevation on the surface
Index contour – bold lines (every 5th line)
Contour interval

## Slide 5
        Ridges = V’s point downhill (towards lower elevation)
        Valleys = V’s point uphill (towards high elevation)

## Slide 6
        Ridges = V’s point downhill (towards lower elevation)
        Valleys = V’s point uphill (towards high elevation)

## Slide 7: Steps for watershed delineation:
  Step 1: identify the outlet and headwater (already labelled in worksheet) **next you may want to roughly mark the high elevation (headwater) and low elevation (outlet) region
  Step 2: identify the high areas (look for closed area/circle) that are close to the river
  Step 3: identify valleys and ridges
        Valleys = V’s point uphill (towards high elevation)
        Ridges = V’s point downhill (towards lower elevation)
  Step 4: draw the streams along the valleys (no need to do for now)
  Step 5: connect the high points and ridges with the outlet with perpendicular line
  ***Watershed delineation is perpendicular to contour lines***

## Slide 9
Water budget
A simple comparison of water supply and atmospheric demand
Water budget = Precipitation (P) − Potential evapotranspiration (PE)
Precipitation (P)
Water coming in
from rain or snow
compared with
↓
Potential ET (PE)
How much water the air
could remove if water is available
If P > PE → water surplus
If P < PE → water deficit

## Slide 10: Get started with the worksheet!
Option to use Excel spreadsheet to graph for question 2
  If you do this option, upload excel spreadsheet to the Canvas assignment “Lab 5”
  Make sure to label axes and differentiate between P and PE
  Label which graph is Champaign, and which is Austin